## Slide 1: BLE Digital Transmitter
Sponsored by
Supervisors
Prof. Hani Fikry Ragaai
Mentors
Eng. Ahmed Hany
Eng. Moaz Khaled
Eng. Abdelrahman

## Slide 2: Presented by
Ahmed Alaa Mohamed Elsodany | 2101434
Sarah Hamed Mahmoud Al Sayed | 2101518
Habiba Essam Eldin Abdelhamid Foad | 2100321
Hanin Ahmed Abdelfattah Ahmed | 2100661
Mina Ayad Younan Bebawi | 2100546

## Slide 3: Table of Content
Introduction
  What is BLE
  System Block Diagram
GFSK
  Traditional FSK
  GFSK Modulation
  GFSK Advantages/Trade-offs
  GFSK Modulation Index
  GFSK BT Product

## Slide 4: Table of Content
Gaussian Filter
  Gaussian Filter as FIR Filter
  Parameters (span/sps)
  Direct VS Transposed Form
  Symmetry Realization for Direct Form
  Implemented Block Diagram
  Results and Observation

## Slide 5: Introduction
Bluetooth Low Energy (BLE) is a wireless standard created to complement Classic Bluetooth, but with a different priority: ultra-low power and low cost rather than high data rate. It’s widely used for short-range connections in IoT and battery-powered devices (wearables, sensors, beacons, smart home), where devices may need to run for months or years on small batteries.
BLE is low-cost since it has:
License-free spectrum: BLE operates in the global 2.4 GHz ISM band, so there are no paid spectrum licenses.

## Slide 6: System Block Diagram

## Slide 7: Traditional FSK Modulation
  In FSK, independent oscillators generate separate in-phase and quadrature components.
  These oscillators switch at the start of each symbol period to create the carrier frequency for modulation.
  However, due to varying amplitudes and phases of the oscillators, abrupt frequency changes occur for every bit transition.
  The modulated FSK signal has a wide spectrum (out of band energy) with non-negligible side-lobes.

## Slide 8: GFSK Modulation
GFSK uses a Gaussian filter (LPF) before modulating the baseband waveform signal (the data signal).
The Gaussian filter smooths out the abrupt frequency changes in FSK(called pulse shaping).
The filter’s impulse response follows a Gaussian function, which narrows the frequency response.
As a result, any sudden frequency shifts are filtered out, making transitions smoother.
The spectral width of the GFSK signal is reduced compared to unfiltered FSK.

## Slide 9: GFSK Advantages/Trade-offs
  Reduced side lobes: GFSK minimizes sideband power and out-of-band spectrum.
  Better spectral efficiency: By shaping the pulses, GFSK achieves improved spectral utilization.
  Constant Envelope: GFSK/FSK modulates only the frequency and not the amplitude, the transmitted signal has a constant envelope. This allows the use of nonlinear power amplifiers (such as Class C or E), which are more energy-efficient — an essential feature for battery-powered devices.
  But…
  While GFSK reduces spectral width, it increases the likelihood of intersymbol interference (ISI) due to spreading in the time domain.

## Slide 10: GFSK Modulation index
Modulation index describes how close should 2 symbols (tones) be without creating ISI.
mathematically defined as:
BLE Specification
For the standard BLE 1M PHY, the specification requires a tight range for h:
0.45≤h≤0.55
Too low modulation indices (<0.3) → narrowest possible bandwidth (best spectral efficiency) but poor demodulation performance (receiver struggles to distinguish the tones).
Too high modulation indices (>1) → better noise immunity but wider spectrum, more adjacent channel leakage (decreases spectral effiency of gaussian filter).
0.5 (GMSK) → sweet spot for BLE: achieves the best possible balance maximum spectral efficiency without compromising the required noise immunity.

## Slide 11: GFSK BT Product
GFSK is characterized by the product , where is the 3-dB bandwidth of the Gaussian filter and is the bit period.
Lower values lead to sharper attenuation of sidelobes, thereby reducing fractional out-of-band power and the 90% bandwidth.
Reducing also lengthens the symbol transition time and therefore increases intersymbol interference (ISI).
A smaller compresses the signal’s spectrum (narrower frequency occupancy) while stretching transitions in time, whereas larger values increase bandwidth but reduce symbol transition time.
The Bluetooth Low Energy 5.4 Core Specification requires a product of 0.5.

## Slide 12: System Block Diagram

## Slide 13: Gaussian Filter as FIR Filter
The Gaussian pulse-shaping filter is implemented digitally as a finite impulse response (FIR) filter:
Once , span, and SPS are selected, the coefficient set is fixed and can be stored in hardware (e.g., Register file).

## Slide 14: Gaussian Filter as FIR Filter
The Gaussian pulse-shaping filter is originally defined in continuous time by a Gaussian impulse response
where the parameter is related to the bandwidth–time product and the sampling period by
Smaller produces a narrower frequency response and therefore a wider impulse response in time (longer transitions), while larger produces the opposite trend. In digital implementation, this continuous-time impulse response is sampled and truncated to obtain FIR coefficients (span and SPS determine the truncation length and sampling density).

## Slide 15: Parameters (span/sps)
Span (symbols) = how long the Gaussian impulse response lasts in time
Larger span → captures more Gaussian “tails” → less truncation error
Tradeoff: more taps → more registers/latency/area
SPS (samples/symbol) = time resolution of the discrete-time model
Higher SPS → smoother, more accurate pulse shape (less discretization error)
Tradeoff: more taps → more computations/hardware
For Even-length (Type II):

## Slide 16: Simulation Results
Span 4 > Span 3: better tail capture in time; cleaner/less truncated shaping
SPS 16 > SPS 8: finer sampling → smoother impulse response and more faithful discrete-time shaping
Selected for primary model: span = 4, SPS = 16 , = 64 taps

## Slide 17: Direct VS Transposed Form
Goal in BLE TX: minimize power (not maximum throughput)
Direct Form
Local dataflow (delay line → MAC) → less switching / simpler routing
No input broadcast → lower fanout
We implement symmetric direct form (folding) to cut hardware
Transposed Form
High throughput (“self-pipelined”)
But input is broadcast to all multipliers → high fanout + more switching → higher power risk
Symmetric Direct-Form FIR used in our implementation (enables multiplier reduction + our multiplier-free logic).

## Slide 18: Symmetry Realization for Direct Form
Gaussian FIR coefficients are even-symmetric (linear-phase): which enables efficient hardware optimization (folding/symmetry).
Instead of multiplying both taps separately, we pair symmetric samples and use one coefficient per pair:
Hardware meaning (Direct-form “folding”)
Delay line provides
For each symmetric pair:
  Pre-adder:
  Single coefficient path: multiply once by
Result: multipliers reduce from to about (adds increase slightly due to pre-adders)

## Slide 19: Implemented Block Diagram
Exploit coefficient symmetry: → pair symmetric samples and use one coefficient per pair
With NRZ input , the pre-adder output is:
so:
Multiplier replacement: Implement this with a small decode +MUX: generate by a left shift (×2), generate by sign inversion/two’s complement, and select between based on the decoded value of .

## Slide 20: Simulation Results

## Slide 21: Table of content
ADPLL Block Diagram
One point modulation at DCO input
One point modulation at TDC input
Two-point modulation
What is TDC
TDC Block Diagram
TDC System operation
Addressing metastability in TDC
Effect of retiming
TDC Within ADPLL
TDC Core
Simulation Results

## Slide 22: ADPLL Architecture

## Slide 23: ADPLL Linear Model

## Slide 24: One Point Modulation at Reference Accumulator
Modulation Transfer function: where

## Slide 25: One Point Modulation at DCO Input
Modulation Transfer function: where

## Slide 26: Two Point Modulation
Modulation Transfer function:
For the case of perfect gain estimation:
r = 1 thus the modulation transfer function is:

## Slide 28: TDC Block Diagram & Operation
The block diagram of the TDC is shown below:
The TDC measures the phase of the reference clock (which will called variable phase) normalized with DCO clock period.
Implemented as a tapped delay line and counters

## Slide 29: TDC Metastability & Mitigation
Reference and DCO clocks (FREF and CKV respectively) are asynchronous
One method to overcome this metastability problem is to oversample FREF with the fast CKV clock

## Slide 30: TDC within ADPLL
The ADPLL diagram with the TDC is shown below.

## Slide 31: Effect of Reference Clock Retiming
Retiming of reference clock carries out ceiling operation where phase measured by CKR is rounded up to the nearest integer as shown in diagrams below for fDCO/fREF = 2.25:

## Slide 32: TDC Core Block Diagram
The number of buffer elements used in delay line (L) >
If too many buffer are used, then circuit consumes more unnecessary area and power.

## Slide 33: TDC Core Operation
tr : delays from last rising CKV edge ( first index of 1 -> 0 in the Q word).
tf : delays from last falling CKV edge ( first index of 0 -> 1 in the Q word).
The number of buffer delays in the one CKV cycle: 2|tf − tr| = Tv

## Slide 34: TDC Core Final Block Diagram

## Slide 35: MATLAB Simulation Setup
A time-domain MATLAB model of the TDC was developed to verify correct functionality and to quantify the measurement error introduced by the TDC
The nominal buffer (tap) delay used in the model is 10ps
The TDC was tested across the DCO frequency range which is 2.16GHz - 2.64GHz
The fractional part of the TDC output was represented with 10 bits
For each selected DCO frequency the model computed the digital phase for 21 consecutive reference cycles to ensure correct accumulation of integer and fractional parts.

## Slide 36: MATLAB Simulation Results
From simulation the maximum error of the TDC is found to be 0.041

## Slide 37: Digital loop filter

## Slide 38: Digital loop filter
DLF processes the phase error signal from TDC and generate a stable control word for the DCO.
The DLF acts like a stabilizer. It smooths out the sharp, noisy, quantized output from TDC.
It converts phase error to frequency control.
Loop filter transfer function: (PI realization)
=>
Ther filter will be composed of Proportional and Integral paths.
Introduction
LOOP
FILTER
Phase Error
OTW

## Slide 39: Digital loop filter
ρ
ρ
Proportional path:
Controls loop bandwidth.
Responsible for fast response.
(PVT variations and initial channel offset)
OTW is directly proportional to phase error.
Integral path:
Accumulates past phase errors
  (to convert phase error → frequency correction).
Eliminates steady-state phase error.
Responsible for fine and accurate tuning.
Improved noise suppression (extra pole).
PI controller

## Slide 40: Digital loop filter
Using s-domain approximation we can get the
closed loop transfer function:
Can be reduced to classical two-pole system transfer function:
Where ζ is the damping coefficient and is the natural oscillation frequency:
Frequency response:
ρ

## Slide 41: Digital loop filter
From previous equations, and are controlled by filter coefficients.
The figure shows The effect of damping coefficient on the loop.
For system to be stable and exhibits acceptable peaking damping coefficient needs to be
At , the system is underdamped and exhibits peaking.
      Magnitude response:

## Slide 42: Digital loop filter
The figure illustrates the closed-loop transfer function for different values of a with constant .
Large α
  Fast response.
  Wider bandwidth.
  Less noise suppression.
Small α
  Slower response.
  Narrower bandwidth.
  Better noise suppression.
Proportional gain tradeoff :

## Slide 43: Digital loop filter
To verify the loop filter functionality and the effect on changing α on the closed loop system, an ideal sample based ADPLL model assuming DCO central frequency = 2.35GHz , target frequency = 2.432GHz
critically damped (Large α) α = , = critically damped (small α) α = , =
Simulation results:

## Slide 44: Digital loop filter
To verify the loop filter functionality and the effect on changing α on the closed loop system, an ideal sample based ADPLL model assuming DCO central frequency = 2.35GHz , target frequency = 2.432GHz
Simulation results:
Underdamped system , α = , =

## Slide 45: Digital loop filter
ADPLL operating modes:

## Slide 46: Digital loop filter
α and loop gain factors are implemented as right-bit-shift operations.
The phase error is sampled at the beginning of type II loop operation and outputs the adjusted phase error to eliminate DC offset from previous mode.
Hardware realization of PI loop filter:

## Slide 47: Digital loop filter
Abrupt α change may cause:
  Large step response.
  Possible loss of lock.
  Overshoot.
  Extended settling time.
Gear shifting is used to change α seamlessly without sharp transitions.
By keeping Normalized Tuning Word (NTW) unchanged before and after the gear shift to maintain frequency continuity.
following two operations are performed simultaneously:
  Add the dc offset to the phase error or the DCO tuning word.
  Reduce the loop constant from α1 to α2.
Gear shifting of proportional gain:

## Slide 48: Table of content
Control Frequency of Digital Oscillators
DCO Operational Modes
DCO Architecture and Implementation
Sign-Sign LMS (SS-LMS)
DCO simulation Result

## Slide 49: DCO

## Slide 50: Control Frequency of Digital Oscillators
A Digitally Controlled Oscillator (DCO) is an oscillator whose output frequency is controlled by a digital control word instead of an analog tuning voltage “VCO”.
For LC tank frequency is determined by:
We control frequency by controlling C
Where :
is fixed capacitor
is the capacitance increment associated with that bit,

## Slide 51: DCO Operational Modes
We are fundamentally limited in frequency resolution by the relation: also fully linear tuning curve would require impractically tight matching between capacitor elements, the DCO operation is divided into three modes.
  PVT Calibration:
  Compensates for PVT
  Coarse frequency tuning with frequency step
  Acquisition:
  Selects target BLE channel frequency
  Intermediate resolution
  Tracking:
  Fine alignment and modulation frequency step
  Highest resolution tuning with Sigma-delta for smoothing
ALL-DIGITALFREQUENCY SYNTHESIZER IN DEEP-SUBMICRON CMOS ROBERT BOGDAN STASZEWSKI

## Slide 52: DCO Architecture and Implementation
  Normalization:
  Converts the normalized tuning word (NTW) into the physical oscillator tuning word (OTW)
  LMS gain calibration:
  estimates the effective DCO gain, so requested deviation matches actual output
  Sigma-Delta:
  high‑resolution frequency steps during modulation

## Slide 53: DCO Architecture and Implementation
  Interface logic:
  Routes the selected tuning words from the different operating modes, applies ZPR and control signals, and delivers a single consistent DCO control word

## Slide 54: Sign-Sign LMS (SS-LMS)
We use sign–sign LMS to estimate the DCO gain.
Faster LMS variants like NLMS need extra logic for a variable step size, which adds power and complexity.
For a low‑power implementation, SS‑LMS offers a good trade‑off between hardware simplicity and calibration performance

## Slide 55: DCO simulation Result
Assumptions for DCO Standalone Validation:
  Fixed capacitor : ±15% PVT variation (≈ ±225 MHz drift).
  Variable capacitors: ideal matching in each mode; PVT variation assumed up to ±30%.
  No loop filter during PVT calibration to keep setup fast.
  Other blocks (phase detector, loop filter, etc.) are modeled as ideal.
  FSK is used instead of GMSK to simplify standalone DCO debugging.

## Slide 56: DCO simulation Result
Simulation results for Ideal situation no PVT change:
Frequency difference from target channel (PVT = 1, without LMS)
Result (PVT = 1, without LMS)

## Slide 57: DCO simulation Result
Comment on Results:
ADPLL did not require PVT calibration.
Offset frequency of 9.91 kHz worst case will be 25KHz
ADPLL FSK modulation waveform (PVT = 1, without LMS)
Simulation results for Ideal situation no PVT change:

## Slide 58: DCO simulation Result
PVT=0.7 and Fixed Capacitor PVT = 0.85 (Without Gain Calibration):
Phase error during lock (PVT = 0.7, with out LMS)
Result (PVT = 0.7,without LMS)

## Slide 59: DCO simulation Result
Comment on Results:
Due to PVT change ADPLL start at 2.66 GHz with offset around 220 MHz
DCO gain error = 28%, limiting deviation to ±180 kHz around channel center. This worsens further with GMSK under PVT variation
PVT=0.7 and Fixed Capacitor PVT = 0.85 (Without Gain Calibration):
ADPLL FSK modulation waveform (PVT = 0.7, without LMS)

## Slide 60: DCO simulation Result
PVT=0.7 and Fixed Capacitor PVT = 0.85 with SS-LMS calibration
ADPLL FSK modulation waveform before gain becomes stable
(PVT = 0.7,with LMS)

## Slide 61: DCO simulation Result
PVT=0.7 and Fixed Capacitor PVT = 0.85 with SS-LMS calibration
ADPLL FSKmodulation waveform before gain becomes stable

## Slide 62: DCO simulation Result
Comment on Result:
LMS starts from an initial gain estimate with an error of 27.964%
As the number of symbols increases, the gain error converges but oscillates around a small non-zero value and never becomes fully stable because of the DCO frequency quantization using sigma delta for further improvement
Gain Error convergence (PVT = 0.7, µ =0.5 )
PVT=0.7 and Fixed Capacitor PVT = 0.85 with SS-LMS calibration

## Slide 63: Sigma Delta

## Slide 64: Table of content
Why sigma delta
First order Sigma delta
Mash Sigma Delta
Operation of MASH 1-1-1
Mitigation of periodicity and IDLE tones
Proposed Sigma Delta Architecture
Simulation Results
Future work

## Slide 65: Why Sigma Delta
  The DCO’s varactor array has coarse frequency steps (LSBs) on the order of tens of kHz, far too large for the sub-Hz or sub-kHz resolution required by the ADPLL.
  A digital sigma–delta (ΣΔ) modulator converts a low-rate fractional tuning word into a high-rate integer sequence whose time-average equals the desired fractional value.
  23 kHz hardware resolution becomes 718 Hz effective frequency resolution improvement could be range of 32
  Sigma delta have 2 main roles which are
    Noise shaping
    Averaging
Robert Bogdan Staszewski, Poras T. Balsara, “All-Digital Frequency Synthesizer In Deep Submicron CMOS” (2006)

## Slide 66: First order MASH Sigma Delta
The error is given by
For constant input the error (our case) is given by :
  If NX is and inetger error will be periodic which will cause idle tones in the frequency domain and this affects the spectrum of the DCO.
  The case NX is a non-integer we will not have the periodic behavior ( irrational number )
First order MASH model
First order MASH linear model (M=1)
K. Hosseini and M. P. Kennedy, “Maximum sequence length MASH delta–sigma, modulators”, IEEE Journal of Solid-State Circuits

## Slide 67: Mash Sigma Delta
Linear model output of the MASH
Noise cancellation network
  It is used in the MASH Sigma Delta modulators to cancel the quantization error of the intermediate stages and its equation is given by:
  The overall transfer function is given by:
  STF = 1 , NTF =
K. Hosseini and M. P. Kennedy, “Maximum sequence length MASH delta–sigma, modulators”, IEEE Journal of Solid-State Circuits

## Slide 68: Operation of MASH 1-1-1
Clock |  |  |  |  |  |  | 
1 | 0.25 | 0.25 | 0.25 | 0 | 0 | 0 | 0
2 | 0.5 | 0.75 | 0 | 0 | 0 | 1 | 1
3 | 0.75 | 0.5 | 0.5 | 0 | 1 | 0 | -1
4 | 0 | 0.5 | 0 | 1 | 0 | 1 | 2
5 | 0.25 | 0.75 | 0.75 | 0 | 0 | 0 | -2
6 | 0.5 | 0.25 | 0 | 0 | 1 | 1 | 3
7 | 0.75 | 0 | 0.25 | 0 | 1 | 0 | -2
8 | 0 | 0 | 0.25 | 1 | 0 | 0 | 1
9 | 0.25 | 0.25 | 0.5 | 0 | 0 | 0 | 0
10 | 0.5 | 0.75 | 0.25 | 0 | 0 | 1 | 1
11 | 0.75 | 0.5 | 0.75 | 0 | 1 | 0 | -1
Clock |  |  |  |  |  |  | 
1 | 0.25 | 0.25 | 0.25 | 0 | 0 | 0 | 0
2 | 0.5 | 0.75 | 0 | 0 | 0 | 1 | 1
3 | 0.75 | 0.5 | 0.5 | 0 | 1 | 0 | -1
4 | 0 | 0.5 | 0 | 1 | 0 | 1 | 2
5 | 0.25 | 0.75 | 0.75 | 0 | 0 | 0 | -2
6 | 0.5 | 0.25 | 0 | 0 | 1 | 1 | 3
7 | 0.75 | 0 | 0.25 | 0 | 1 | 0 | -2
8 | 0 | 0 | 0.25 | 1 | 0 | 0 | 1
9 | 0.25 | 0.25 | 0.5 | 0 | 0 | 0 | 0
10 | 0.5 | 0.75 | 0.25 | 0 | 0 | 1 | 1
11 | 0.75 | 0.5 | 0.75 | 0 | 1 | 0 | -1
The table shows the internal signals and output of a MASH 1-1-1 sigma–delta modulator with an input 0.25, illustrating how the final output is formed by combining the three cascaded stages.

## Slide 69: Mitigation of periodicity and IDLE tones
Dither bits are added at the accumulator input to break this periodicity and suppress spurs. Traditional LFSR-based dither raises the low-frequency noise floor and this could affect the PSD, there are different topologies to implement this which includes :
  Filtered dither (first order dither)
  Eliminable dither (Dither is injected in 2 points in the system to be cancelled by the noise cancellation network)
  XOR based dither ( XOR dither at the input of the second accumulator and feeding forward the first accumulator output to the third accumulator input)
Modified sigma delta (HK-MASH) which contains an additional feed back path scaled by the coefficient α is introduced to guarantee maximum sequence-length operation for all constant inputs. This may have some drawbacks that is introducing poles and overestimating the fractional part.

## Slide 70: Proposed Sigma Delta Architecture
Modified dither MASH Digital implementation
Modified dither MASH Linear model

## Slide 71: Simulation Results
Power spectral density (PSD) of the MASH 1-1-1 output for an irrational input value . The spectrum shows no periodic tonal components, as the irrational input prevents repetitive patterns in the quantization process.
Extended output spectrum of the MASH 1-1-1 modulator for a rational input value (0.25). Strong periodic tonal components are clearly visible, resulting from the repetitive nature of the rational input sequence. The application of dithering significantly reduces these tones by breaking the periodicity.

## Slide 72: Simulation Results
Input | Architecture | Output | Error
0.75 | Modified MASH | 0.75294 | 0.00294
 | Modified Dither | 0.75 | 0
 | Normal Dither | 0.75001 | 0.00001
 | Original MASH | 0.75 | 0
0.255 | Modified MASH | 0.25601 | 0.00101
 | Modified Dither | 0.255 | 0
 | Normal Dither | 0.25499 | 0.00001
 | Original MASH | 0.255 | 0
 | XOR-based Dither | 0.25499 | 0.00001
0.000051 | Modified MASH | 0.00006 | 0.000008
 | Modified Dither | 0.00004 | 0.000012
 | Normal Dither | 0.002 | 0.001948
 | Original MASH | 0.00006 | 0.000008
 | XOR-based Dither | 0.00007 | 0.000018

## Slide 73: Future Work
Integrate the MATLAB behavioral models of all system blocks into a complete ADPLL/DCO system-level model.
Run Monte Carlo simulations to select robust loop-filter and LMS parameters.
Introduce key non-idealities for each block, including noise, mismatch, quantization effects, and PVT corners.
Develop a comprehensive verification plan defining coverage goals, test scenarios, corner cases, and pass/fail criteria for system- and block-level validation.
Begin RTL design of the digital blocks, followed by synthesis and timing closure.
Insert DFT structures to enable product testability.
Perform formal verification to ensure functional correctness and design robustness.

## Slide 74: Thanks